16X2 LCD DRIVER

1st Level Implementation.

EXPECTIATION:

- Display 32 charachters in sequence. Take a charachter or a string with string length less than 32 from user space program and Display.
- If String is more than 32 charachters just ignore the exceeding charachter.

OPERATION AVAILABLE TO USER PROGRAM:
- Open
  This Function should initialise the LCD hardware. LCD should blink its back light twice and show string “INIT DONE !!”
- Write
  This Function should accept string less than 32 chars, If user enter more charachter than it should not fail, It should show the 32 chars and ignore rest.
- Close
  This function should display “PWR OFF !!” blink back light and power off the device.

INTERFACES:

SET OF API’s:

LCD_Init()
Register LCD device in kernel
Set the LCD in 8 bit mode
Blink the back light and display “INIT DONE !!”

- LCD_Exit()
  Unallocate the resources
  Blink the back light and display “PWR OFF”
  Unregister the LCD device from kernel
- LCD_Send_Command(Command)
  Set the LCD in command by following the below steps
Reset the RS pin of LCD i.e (RS = 0, Instruction Register)
Put the command on DB line
Set E pin as 1 wait 5 sec and than set as 0

- LCD_Send_Data(string)
  Set the LCD in command by following the below steps
  Reset the RS pin of LCD i.e (RS = 1, Data Register)
  Put the char on DB line
  Set E pin as 1 wait 5 sec and than set as 0
  till the last char in string if it is less than 32 or till 32 char.
  `
- LCD_Blink()
- LCD_Delay(seconds)